## Slide 1
pvaSrv
CA
pvAccess Client
pvAccess
Channel Access Client
rSrv
IOC database
Device I/O
IOC
Notes: The simplest thing you can do with EPICS V4 – add the pvAccess server to an IOC.
So the first thing we see is that in EPICS V4, at core, the IOC remains the same. An EPICS Version 4 IOC is just an EPICS Version 3 IOC with a pvAccess Server added.
To be honest, there is not much advantage in using just this configuration for EPICS installations which are already heavily invested in EPICS Channel Access, since all your existing clients will be using Channel Access. For such places, the advantages of EPICS V4 will stem more from the basic architectures in the following 2 or 3 slides, and for new work.
But for new institutions, just now building your EPICS installation, you may consider this architecture.
ESS for instance, is going to be all pvAccess.
[ADD: pvaSrv example]

## Slide 2
pvAccess Client
pvAccess
CA
Channel Access Client
IOC database
Device I/O
CA
IOC
pvaSrv
rSrv
Notes: Just to add, the client side library of EPICS V4 includes support for Channel Access.
In fact, more generally, the pvAccess API includes a plugable architecture for “channel providers”, of which the pvAccess protocol and the Channel Access protocol are two.
[ADD example of getting CA data with pvAccess API – pvget –p ca]

## Slide 3
pvAccess Client
pvAccess
CA
Channel Access Client
CA
IOC
Device drivers etc stay
only under IOC database
IOC database
Device I/O
pvDatabase
pvaSrv
rSrv
Notes: Now things get interesting for new kinds of work made easier by EPICS Version 4.
V4 adds a new kind of front end processing database, the “pvDatabase”.
The device I/O, particularly the device driver layer, remains under the IOC Database.
This slide illustrates the architecture in which a pvDatabase is used inside an IOC. But a pvDatabase can be used standalone, at the host level of an EPICS version 4 controls network. At that level it might be used to aggretage data from a number of Channel Access PVs in subordinate IOCs, like to gather data from a number of beam diagnostics and deliver it all as one package.

## Slide 4
pvAccess Client
pvAccess
CA
Channel Access Client
CA
IOC
IOC database
Device I/O
pvAccess Server
BYO back-end datasource
pvDatabase
pvaSrv
rSrv
Notes: The last major architecture addition offered by EPICS Version 4, is to add the basis of service oriented architecture. The getRPC method of pvAccess allows a client to send arguments along with the PV. The arguments are then used for synchronous processing, and the results then returned.
Indeed, the same PV can be used both the monitor setup and in the RPC setup, allowing for one logical quantity to be acquired from either context – the result of a monitor of some system, or the result of a specific computation based on arguments. For instance, in an accelerator model, the PV for the beta function of a beampath may be continuously computed according to defaults – such as the default timing configuration, or it may be required to be computed from a specific timing configuration. The default case can be monitored, but the special case can be requested by RPC.
RPC is also very useful for connecting PVs to backend databases like MongoDB, mySql, Oracle etc. This is used at SLAC, ESS and NSLS-II.